## Slide 1
Chart: 
Hearts'n'Waves
Hierarchical ECG Intelligence System on STM32
Low-power, event-driven, three-level architecture with a live Python digital twin
Notes: Introduce the project: a wearable-style ECG monitor where the STM32 does the intelligence on-chip in three levels, and a Python app on the PC acts as a digital twin display.

## Slide 2
The Problem
Hearts'n'Waves | Hierarchical ECG on STM32
2
PROBLEM STATEMENT
Continuous ECG monitoring can consume significant computational resources and easily consume power. This is especially important for wearable devices.
Design a hierarchical ECG intelligence system for the STM32.
Compute is limited
Running heavy analysis on every 5 ms sample wastes CPU cycles on a small MCU.
Battery is small
An always-awake CPU and constant data streaming drain a wearable quickly.
Our answer: hierarchy
Cheap stages run always; costlier logic runs only when an event (a beat) occurs.
Notes: Restate the problem statement. The key idea is that not every sample needs the same amount of work: filter cheaply, detect beats, and only classify when there is something to classify.

## Slide 3
Three-Level Architecture
Hearts'n'Waves | Hierarchical ECG on STM32
3
SENSE
12-bit ADC read by a 200 Hz timer ISR. Leads-off and temperature inputs.
LEVEL 0
Band-pass IIR filter removes drift and noise. Runs every sample.
LEVEL 1
Pan-Tompkins beat detector gives BPM and HRV. Runs every sample.
LEVEL 2
Decision tree: Normal, Warning or Critical. Runs on a beat or every 250 ms.
UART
One CSV line: ECG, BPM, Temp, Class, HRV at 115200 baud.
DIGITAL TWIN
Python live ECG strip, status HUD, estimated SpO2 and BP.
Runs on the STM32 (embedded)
Runs on PC
Notes: Walk left to right. Levels 0, 1 and 2 all live on the STM32. The rule is: the cheapest stage sees every sample; each later stage runs less often. The PC only visualises what the chip already decided.

## Slide 4
Sampling and Hardware Layer
Hearts'n'Waves | Hierarchical ECG on STM32
4
Pin | Function
PA0 | ECG analog input (12-bit ADC)
PA1 | Temperature analog input
PA3 | LO+ leads-off detect
PA2 | LO- leads-off detect
TIM3 @ 200 Hz
The timer interrupt only reads the ADC and raises a flag. All processing happens in loop(), keeping the ISR tiny.
1
Sleep
loop() calls __WFI(), halting the core until the next interrupt.
2
Sample
TIM3 fires every 5 ms: the ISR reads PA0 and sets sampleReady.
3
Guard
On wake, check LO+/LO-. If electrodes are off, send status and return early.
4
Process
Otherwise run Level 0, Level 1 and (if needed) Level 2, then sleep again.
Notes: The timer gives deterministic 200 Hz sampling (5 ms period). Between samples the CPU sleeps in WFI. The leads-off guard is the first power saver: no DSP is done when there is no signal.

## Slide 5
Where the Power Is Saved
Hearts'n'Waves | Hierarchical ECG on STM32
5
Chart: UART packets per second (approx.)
| Stream every sample | Event-driven (ours)
Packets per second | 200 | 5
Ours: at most ~4 periodic packets plus 1-2 beat packets per second at rest. Baseline is a hypothetical per-sample stream.
Sleep between samples
__WFI() idles the core between 200 Hz timer ticks.
Early exit on leads-off
No filtering or detection without a signal; status sent at most every 200 ms.
Events, not streams
Classifier and UART run on a detected beat or every 250 ms, not per sample.
Tiny arithmetic
Fixed buffers and a few multiply-adds per sample. No heap, no FFT.
Notes: This directly answers the power question. Sampling is timer-driven with sleep in between; the expensive pieces (classification and communication) are gated on events. Compared with streaming every sample over UART, the packet rate drops by roughly 40x.

## Slide 6
Level 0: Band-pass Filter
Hearts'n'Waves | Hierarchical ECG on STM32
6
Second-order IIR difference equation
y[n] = 0.2929*x[n] - 0.2929*x[n-2] + 0.5858*y[n-1] - 0.1716*y[n-2]
2nd order
IIR band-pass filter
4
multiplies per sample
4
state variables: x1, x2, y1, y2
Why filter first? Baseline wander and high-frequency noise would cause false beats in Level 1. This stage costs the same tiny amount for every sample, so it is cheap enough to run always.
Notes: Level 0 is the always-on, constant-cost stage. It keeps only four past values, so memory and compute are negligible.

## Slide 7
Level 1: Pan-Tompkins Beat Detection
Hearts'n'Waves | Hierarchical ECG on STM32
7
1 Derivative
5-point filter highlights the steep QRS slope.
2 Squaring
Makes slopes positive and boosts large ones.
3 Moving window
30 samples (150 ms) average gives an energy envelope.
4 Adaptive threshold
Starts at 1800, floor 1200. Updated 0.7/0.3 per beat, decays x0.997.
Beat validation
550 ms refractory lockout after each beat
Accept only RR intervals giving 45-120 BPM
BPM smoothed: 0.85 x old + 0.15 x new
HRV (RMSSD)
Keeps the last 5 RR intervals
Root-mean-square of successive differences
Feeds Level 2 (HRV < 15 ms = Warning)
Notes: Classic Pan-Tompkins in four steps, implemented with fixed-size buffers. The refractory period and the BPM gate reject double-counting and noise. Only when a valid beat is found do we update BPM and HRV.

## Slide 8
Level 2: On-Device Decision Tree
Hearts'n'Waves | Hierarchical ECG on STM32
8
INPUTS
BPM, Temp, HRV
+ leads-off
CRITICAL
class 2
Checked first
BPM < 45 or > 140, Temp > 39 or < 34 C, or leads off (BPM <= 0)
WARNING
class 1
Checked second
BPM < 55 or > 105, Temp > 37.8 C, or HRV < 15 ms
NORMAL
class 0
Otherwise
All values inside the safe ranges
Notes: Level 2 is a hand-written decision tree: a few comparisons, no floating-point heavy work. It is only evaluated on a beat or every 250 ms. The class number (0, 1, 2) is sent to the PC, so the PC does not need to redo the analysis.

## Slide 9
Level 2 to PC: UART Data Protocol
Hearts'n'Waves | Hierarchical ECG on STM32
9
# normal beat
-12.4,74.2,36.9,0,34.5
# warning
-3.1,108.0,37.2,1,12.8
# leads off
0.0,0.0,36.9,2,0.0
Rate-limited on purpose
A line is sent on a detected beat or every 250 ms. Leads-off status goes out every 200 ms. Serial output is 115200 baud text.
# | Field | Used by Python for
0 | Filtered ECG | Received, not plotted
1 | BPM | Sets waveform speed, HUD
2 | Temp (C) | Smoothed, shown in HUD
3 | Class 0/1/2 | Status text and colour
4 | HRV (ms) | Shown in HUD
Notes: The protocol is a five-field CSV line. Field 0 (the filtered ECG sample) is sent but the current Python code does not plot it; it draws a synthesized PQRST instead. The class field carries the on-chip decision.

## Slide 10
Python Digital Twin (digital_twin.py)
Hearts'n'Waves | Hierarchical ECG on STM32
10
1 Read UART
Reads pending bytes, keeps the newest line, parses BPM, Temp (EMA 0.9/0.1), Class, HRV.
2 Phase generator
Advances cardiac phase by BPM/60 x dt each loop, wrapping at 1.0: one cycle per heartbeat.
3 PQRST synthesis
Sum of five Gaussians (P, Q, R, S, T) plus noise gives one ECG sample per loop.
4 Rolling strip
A deque holds 800 samples (4 s x 200 Hz), drawn as a scrolling clinical strip.
5 Throttled render
Plot redraws at about 30 FPS and the HUD at 2 Hz, avoiding lag and freezes.
6 Twin metrics
SpO2 and systolic BP are model estimates from BPM and temperature, not measured.
Notes: The PC side never re-detects beats. It trusts the BPM and class from the chip, generates a clean waveform at that heart rate, and updates a heads-up display. Throttled drawing keeps the laptop responsive.

## Slide 11
How the Waveform Is Synthesized
Hearts'n'Waves | Hierarchical ECG on STM32
11
Chart: One synthesized cardiac cycle (phase 0 to 1)
Wave | Amp (mV) | Centre | Width
P | 0.12 | 0.12 | 0.022
Q | -0.12 | 0.22 | 0.007
R | 1.20 | 0.24 | 0.008
S | -0.30 | 0.26 | 0.010
T | 0.22 | 0.45 | 0.045
wave = A * exp( -((phase - centre) / width)^2 )
Leads disconnected: the trace falls back to a flat baseline with tiny noise and a red warning.
Notes: Each wave is a Gaussian bump at a fixed position in the cycle. R is tall and narrow, T is low and wide. Adding Gaussian noise makes it look like a real strip. This is a visualisation of the heart rate, not the raw signal.

## Slide 12
Summary
3
levels of intelligence: filter, detect, classify
200 Hz
timer-driven sampling with sleep in between
~40x
fewer UART packets than streaming every sample
Cheap work runs always. Costlier work runs only on events. The PC just displays the result.
Thank you
Notes: Close by tying back to the problem statement: a hierarchical design keeps compute and power low for a wearable, while still giving useful clinical-style alerts.